## Slide 1: Designing Concurrent Software
Making good decisions

## Slide 2: Two reasons for concurrency
We write concurrent code for two reasons
  Maintain responsiveness during long operations
  Divide work to accomplish more in less time
Writing concurrent code is difficult – don’t do it for any other reasons.

## Slide 3: Patterns for responsiveness
I’ve seen three patterns occur often
  Ad-hoc background thread
    Expensive work is done on the background thread
    Main thread only remains responsive for the user
  Long running background thread(s)
    Assigned tasks by producer/consumer queue
    Background thread is a while loop
    Exits when main thread signals it via condition variable or atomic
  Command/query on independent threads
    Either takes lock on data and executes to completion
    Command mutates data, query reads data

## Slide 4: Example: ad-hoc background thread
The GUI application which computes the value of pi uses this approach.

## Slide 5: Example: Long running thread
Useful for two-way synchronization between two GUIs.
Application 1
Application 2
Call method and wait for response
Fire event and wait to be processed (no response)
GUI Thread
GUI Thread

## Slide 6: Example: Long running thread
Use producer/consumer queue to push events off GUI thread
Application 1
Application 2
Call method and wait for response
Fire event and wait to be processed (no response)
GUI Thread
GUI Thread
Consumer Thread
Producer
Fire event and don’t wait to be processed

## Slide 7: Command/query model
Divide actions on data into reads and writes
  Command write (or mutate) data
  Queries read data
  Each command or query locks the data it will use, then executes
Provides flexibility
  A command or query may execute
    On GUI thread
    On a background thread with a GUI wait
    On a background thread with the GUI continuing

## Slide 8: Guidelines for responsiveness
These patterns are relatively well established
  Used prior to pervasive multi-processing machines
  Many libraries have these patterns built in
Guidelines
  Write code sequentially, design a clean API, test it.
  Apply one of the known patterns to execute it on a separate thread.
  The domain-specific code and the threading code should not mix.

## Slide 9: Divide work to accomplish more
As multi-processor systems become pervasive taking advantage of those processors becomes important.
  If task x requires time A to complete using one processor, can we use n processors to complete x in A/n time?
  We can divide the work in x one of three ways
    Prior to executing x, partition in input data and perform x1, x2, x3, etc.
    During the execution of x, partition the input data and perform x1, x2, x3, etc.
    If x is a sequence of steps, perform each step in parallel on a stream of data
  Approaches 1 and 2 parallelize based on data
  Approach 3 parallelizes based on the algorithm

## Slide 10: Partitioning input data
Often referred to as map-reduce or task-based parallelism
  The map portion partitions the data and performs task x on each partition.
  The reduce portion combines the output of each task x.
Imagine we want to find the average of a list of numbers:
42 | 4 | 5 | 18 | 931 | 6 | 2 | -67
Thread 1
42 + 4 = 46
Thread 2
5 + 8 = 18
Thread 3
931 + 6 = 937
Thread 4
2 + -67 = -65
map
Main Thread
(46 + 18 + 937 + -65) / 8 = 117
reduce

## Slide 11: Partitioning during execution
Some algorithms require inspection of the data to partition it.
  Quicksort recursively sorts subsections of the input
  Each recursive call operates on an independent partition of the data
  Each call can execute on a separate thread
42 | 4 | 5 | 18 | 931 | 6 | 2 | -67

## Slide 12: Dividing work by task type
Many algorithms have a independent sequence of steps
  Each part of the data may be an input to each step
  The steps operate on a sequence of data
  Each step can be executed on a separate thread.
  This is often called pipelining.
42 | 4 | 5 | 18 | 931 | 6 | 2 | -67
Thread 1
Step 1
18
Thread 1
Step 1
5
Thread 1
Step 1
4
42
931

## Slide 13: What is the best approach?
It depends on the situation!
  Dividing work by task type
    All of the patterns for responsiveness are special cases.
    High frequency trading algorithms often operate on a stream of data.
    Limits scalability, but requires known hardware
  Partitioning during execution
    Tied to specific algorithms
    Difficult to determine hardware requirements
  Partitioning input data
    Usually input data is known and can be partitioned
    Offer best chance to scale in the future

## Slide 14: Performance vs. Scalability
These are two related, but different concepts.
  Performance: the time an action takes to complete
  Scalability: how the performance changes with more resources or a larger problem
We have already seen the he need for increased performance has pushed CPU designs to more processors and cores.
  Partitioning input provides the best potential for scalability
  Therefore, it provides the best potential for future performance

## Slide 15: Amdahl’s Law
Amdahl’s law relates performance and scalability.
  Given a certain number of processors, what is the expected performance gain?
  Helps us understand the benefit of making code parallel.
  P is the expected performance gain
  N is the number of processors
  fs is the fraction of the program which is serial

## Slide 16: Exploring Amdahl’s law
If fs, is zero (no serial code)
  Then P = N, each processor is used a full efficiency
  Called and embarrassingly parallel algorithm
If fs, is one (no parallel code)
  Then P = 1, each processor is used at zero efficiency
  The algorithm will not benefit at all from more processors
More likely, fs, is something like 0.3 (30% serial code)
  The benefit of additional processors is bounded

## Slide 17: Plot of Amdahl’s Law
Chart: Amdahl's Law for values of fs
| 1 | 2 | 3 | 4 | 6 | 7 | 8 | 9 | 10 | 11 | 12 | 13 | 14 | 15 | 16 | 17 | 18 | 19 | 20
P (fs = 0.01) | 1 | 1.9802 | 2.9412 | 3.8835 | 5.7143 | 6.6038 | 7.4766 | 8.3333 | 9.1743 | 10 | 10.8108 | 11.6071 | 12.3894 | 13.1579 | 13.913 | 14.6552 | 15.3846 | 16.1017 | 16.8067
P (fs = 0.05) | 1 | 1.9048 | 2.7273 | 3.4783 | 4.8 | 5.3846 | 5.9259 | 6.4286 | 6.8966 | 7.3333 | 7.7419 | 8.125 | 8.4848 | 8.8235 | 9.1429 | 9.4444 | 9.7297 | 10 | 10.2564
P (fs = 0.1) | 1 | 1.8182 | 2.5 | 3.0769 | 4 | 4.375 | 4.7059 | 5 | 5.2632 | 5.5 | 5.7143 | 5.9091 | 6.087 | 6.25 | 6.4 | 6.5385 | 6.6667 | 6.7857 | 6.8966
P (fs = 0.2) | 1 | 1.6667 | 2.1429 | 2.5 | 3 | 3.1818 | 3.3333 | 3.4615 | 3.5714 | 3.6667 | 3.75 | 3.8235 | 3.8889 | 3.9474 | 4 | 4.0476 | 4.0909 | 4.1304 | 4.1667
P (fs = 0.3) | 1 | 1.5385 | 1.875 | 2.1053 | 2.4 | 2.5 | 2.5806 | 2.6471 | 2.7027 | 2.75 | 2.7907 | 2.8261 | 2.8571 | 2.8846 | 2.9091 | 2.931 | 2.9508 | 2.9688 | 2.9851
P (fs = 0.4) | 1 | 1.4286 | 1.6667 | 1.8182 | 2 | 2.0588 | 2.1053 | 2.1429 | 2.1739 | 2.2 | 2.2222 | 2.2414 | 2.2581 | 2.2727 | 2.2857 | 2.2973 | 2.3077 | 2.3171 | 2.3256
P (fs = 0.5) | 1 | 1.3333 | 1.5 | 1.6 | 1.7143 | 1.75 | 1.7778 | 1.8 | 1.8182 | 1.8333 | 1.8462 | 1.8571 | 1.8667 | 1.875 | 1.8824 | 1.8889 | 1.8947 | 1.9 | 1.9048