## Slide 1: Dennard Scaling
Why the future will be different

## Slide 3: What does Moore’s law really say?
In 1965 Gordon Moore wrote an article for Electronics Magazine
  He was asked to predict the next ten years of semiconductor development
  Stated that the number of transistors would double each year.
  Revised in 1975 to double every two years.
Moore didn’t know exactly why this was the case
  He was viewing historical trends
In fact, shrinking dimensions on an integrated
structure makes it possible to operate the structure at
higher speed for the same power per unit area.

## Slide 4: The reason Moore’s law works
In 1974, Robert Dennard and his team explained the trend Moore witnessed
  Dennard Scaling
    All important factors in transistor design scale down by the same constant
    As they scale down, the electric field in the channel remains constant
  Making transistors smaller made them better
    Transistor density increased
    Transistor switching delay decreased
    Transistor power usage decreased

## Slide 5: Dennard Scaling
Gate
Source
Drain
Oxide
Tox
L
V
Gate
Source
Drain
Oxide
aTox
aL
aV
a =1/k
Device or Circuit Parameter | Scaling Factor
Device Dimension Tox, L, W | 1/k
Voltage | 1/k
Current | 1/k
Capacitance | 1/k
Delay time | 1/k
Power Dissipation | 1/k2

## Slide 6: The end of Dennard scaling

## Slide 7: Why is Dennard Scaling ending?
Oxide thickness (Tox) can only get so small
  65 nm – Tox is 5 atoms thick
  Intel has moved from 45 nm, 32 nm, and is now at 22 nm
  Scaling is getting more and more difficult
Leakage current is now a problem for power consumption
Power = CEFF VDD2 f + ILEAK VDD

## Slide 8: Hardware Solutions: transistor design
New transistor manufacturing techniques
Classic Transistor
Intel’s Tri-Gate Transistor

## Slide 9: Transistor design will continue

## Slide 10: Hardware Solutions: Lower Power
Power has become the leading optimization factor in two important places
  The data center – due to large scale
  Mobile devices – due to batteries
Options for power optimization
  Turn off transistors when they are not used to eliminate loss due to leakage current
  Lower VDD
  Optimize power and performance together

## Slide 11: What does all of this mean for software?
Three key conclusions (or maybe guesses)
End of transistor delay scaling
+
Moore’s Law
More CPUs and increased parallel capability
Power vs. Performance Optimization
Heterogeneous hardware:
Fast and expensive
Slow and cheap
Lower VDD
Unreliable results