## Slide 1: Dennard Scaling
Why the future will be different

## Slide 3: What does Moore’s law really say?
In 1965 Gordon Moore wrote an article for Electronics Magazine
  He was asked to predict the next ten years of semiconductor development
  Stated that the number of transistors would double each year.
  Revised in 1975 to double every two years.
Moore didn’t know exactly why this was the case
  He was viewing historical trends
In fact, shrinking dimensions on an integrated
structure makes it possible to operate the structure at
higher speed for the same power per unit area.

## Slide 4: The reason Moore’s law works
In 1974, Robert Dennard and his team explained the trend Moore witnessed
  Dennard Scaling
    All important factors in transistor design scale down by the same constant
    As they scale down, the electric field in the channel remains constant
  Making transistors smaller made them better
    Transistor density increased
    Transistor switching delay decreased
    Transistor power usage decreased
Source: Rob Rutenbar

## Slide 5: Dennard Scaling
Gate
Source
Drain
Oxide
Tox
L
V
Gate
Source
Drain
Oxide
aTox
aL
aV
a =1/k
Device or Circuit Parameter | Scaling Factor
Device Dimension Tox, L, W | 1/k
Voltage | 1/k
Current | 1/k
Capacitance | 1/k
Delay time | 1/k
Power Dissipation | 1/k2